Agricultural ELECTRICIfication CAREER DEVELOPMENT EVENT

REVISED 1-17-12

Sponsored by Electric Cooperatives of Arkansas

The objectives of the Electrification Career Development Event are:

- Develop an understanding of, and appreciation for, the importance of adequate wiring of the successful operation of electrical equipment.

- Develop certain skills in wiring.

- Create a desire to gain knowledge in the use of proper wire size, circuit protection and wiring devices which constitute a safe and adequate wiring job.

- Increase knowledge of electrical usage which will promote additional comfort and labor saving equipment in the home and on the farm.

5.	Promote leadership ability by disseminating information on  electrical  equipment usage.

#### THE CONTEST

A team will consist of 4 members who will work individually through the contest.  Each member will take the written test and one member will be randomly assigned to one practicum by the contest official.  It will be necessary for all team members to be competent in all areas of the contests.  All 4 team member scores will count for total team score.  There will not be a drop score.

#### CONTEST FORMAT

PART I—General Knowledge Test (All team members)

Fifty (50) objective type, multiple choice questions will be selected from the contest references.  The questions will come from Electrical Wiring  (AAVIM) and Basics of Electrical Motors (AAVIM), Electrical Controls (AAVIM) and Understanding Electricity (AAVIM).  The test will measure the contestant’s knowledge and understanding of basic electricity, electric motors, wiring, safety and planning.  All team members will take the test.

Time:  Sixty (60) minutes will be allocated for the written test.

Scoring:  Each question shall be worth 2 points for a total of 100 points.

PART II–Practicums

This phase will consist of four (4) practicums.  Contestants will each perform only one practicum as designated by the contest official.

Time:  Each practicum will have forty (40) minutes allocated for completion.

Scoring:  The maximum score for each practicum will be two hundred (200) points.  Each practicum will be scored independently using the score sheet for that particular practicum.

#### PRACTICUM DESCRIPTION

# PRACTICUM I –WIRING DIAGRAM

One member of each team will be given a problem stating how certain devices are to be wired according to the NEC.  The devices will be shown and the contestant will be asked to draw the circuits showing the connections to each device so they will operate properly.  Care should be taken to show the connections clearly and accurately.  Colored pencils or pens as shown below will be used to represent the different colored wires.

Black-------------------------------------------------------Energized wire

Red---------------------------------------------------------Energized wire

Blue--------------------------------------------------------Neutral

Green------------------------------------------------------Ground

Blue w/ black mark------------------------------------White wire used as energized wire

(black mark indicates black tape wrapped around white wire)  See example

A typical problem is shown on the following page.

The contestant will be given 40 minutes to diagram up to eight of the devices listed below:

- Lights and/or receptacles controlled by:

- Single pole switch

- Three-way switches

- Four-way switches

- Duplex receptacle

- 240 volt special purpose outlet

- Doorbell

- Split-wired (two circuit) receptacles—one or both circuits-switch controlled

- Circuit for 120volt/240 volt motor

- GFCI and GFCI protected receptacles

The contestant should show connection of wire in the panel and label breaker with proper amperage.  Also, they will be asked to describe wire correctly according to type, size, and number of wires.

Contestants must provide their own colored pencils or pens.

# -EXAMPLE-

# Name ___________________ School __________________Code/Color _____

## Score ________

Arkansas FFA Electrification Contest

Electrical Diagram

### 200 Points

Using colored pencils, draw the wiring diagram on the attached sheet for the devices so that they will function properly.  Use black and red lead pencils for energized wire, blue lead for the neutral, and green lead for the bare ground.  Blue, in this case, is used instead of the white for the neutral so it will be legible. Use one of the attached sheets for your work or scratch sheet.  The finished diagram to be graded should be shown on the other sheet.  Be sure that the finished diagram is legible.

# The following device is to be diagrammed

- Using one 120-volt circuit, diagram a light controlled from one location and a duplex receptacle that is always hot. It is required to show proper attachment in the panel.  (150 points)

- Show the recommended amperage and voltage rating on the breaker in the panel to protect the circuit.  Also, indicate the type, size, and number of wires recommended. (50 Points)

1.        Circuit Parts

Neutral--------------------------50 points      	_________

Energized----------------------50 points	_________

Grounding----------------------50 points	_________

2.	Wire Type--------------------------------10 points	_________

Wire Size---------------------------------10 points	_________

Number of Wires-----------------------10 points	_________

Breaker Amperage---------------------10 points	_________

Breaker Voltage------------------------10 points	_________

Total Points	(200)		_________

# PRACTICUM II—WIRING PRACTICE

This practicum will consist of actual wiring some of the devices mentioned in Practicum I. This will be limited to a maximum of 4 boxes and 5 devices.

One member of each team will be provided with an incomplete diagram and written description of circuit(s) to be wired.  The wiring exercise will be completed in a work area assigned to the contestant.  Scoring will be done on the wiring skills demonstrated in the allotted 40 minutes. The contestant must clean work area when finished, but does not have to dismantle wiring board.

The contestant will provide a wiring board as specified below with the following boxes attached as shown in drawing: 1) 3 switch or utility boxes  2) 1 double gang switch box  3) 2 round or octagon boxes, and 4) 1 surface mount dryer plug.  The boxes should be metal and include connectors or have anchoring clamps in them.  The board should be approximately 2’ x 4’ and it is suggested that some sort of handle be attached to it.

Contestants must also bring the following devices and material:

- 16' of NMSC 12-2 w/g, 8' of NM 12-3 w/g, 16' of NMSC14-2 w/g, 8' of 14-3 w/g,

4' NMSC 10-2 w/g or 10-3 w/g{depending on what type of 30A dryer plug you have) All cable must be unstripped and intact, no precut with hooks.

NOTE:  In order to minimize expenses, 14 guage wire may be substituted for 12 guage wire in 120V circuits where NEC normally requires 12 guage.  Any 240V circuit wired should use proper wire size required by NEC.

- 3 SP switches, 3 DCO’s, 1 GFCI duplex receptacle, 1 20A/240V SPO, 1 DPST 20A/240V switch, 2 three-way switches, 1 four-way switch, 2 light receptacles, electrical tape, jumper wires, and either ground clips or ground screws for each box.

- Contestants will provide their own tools.  The tools used are at the contestant’s discretion, but the following tools are recommended:  Lineman’s pliers, needlenose pliers, knife, wire stripper and flat blade screwdriver.

# -EXAMPLE-

# Name _____________________ School _________________Code/Color____

## Score ________

Arkansas  FFA Electrification Contest

Wiring Practice

### 200 Points

Forty (40) minutes will be allowed to complete the contest.

Work area should be clean before leaving.

No points will be awarded if contestant does not attempt the skill.

Problem:  Using one source of electricity, wire one light to be controlled from one location . Source wire should enter light box.  You may use the attached worksheet to plan, if needed.

Score Card:

Points	            Score

Insulation removal			  20			_______

Anchor to box			  20			_______

Splices (must be hard spliced; no wire nuts)	  30			_______

Wire loops				  20			_______

Grounding				  30			_______

Color code				  30			_______

Amount correctly completed	  50			_______

Total Points	(200 possible)				_______

EXAMPLE

# WIRING PRACTICE

# PRACTICUM III—WIRING PLAN

This practicum will consist of completing a wiring plan for one of the following applications: Utility Room, Kitchen, or a Shop.  Contestants should draw the proper location of given devices on plan using

proper electrical symbols.  A circuit sheet must also be completed identifying each circuit and specifying breaker amperage, wire type, wire size, and number of wires.

- Contestants should not put more than 8 loads on a general purpose circuit.

- Individual circuit items should be designated using a SPO symbol

and labeled with a subscript according to equipment.

- Contest officials must specify either wattage or horsepower and voltage for shop equipment, water heaters, and heaters

- Utility room—Possible examples include:

- 1000W 240V Electric water heater

- Electric clothes dryer

- Clothes washer

- Food freezer

- 6000W 240V Electric heater

- Convenience outlets

- General lighting

- Kitchen—Possible examples include:

- Free standing electric range

- Dishwasher

- Refrigerator/freezer

- Small appliance outlets

- 750 watt 120V microwave oven

- Vent hood

- Garbage disposal

- Convenience outlets

- General lighting

- Lighting over sink

- Shop—Possible examples include:

- Electric welder

- 2 h.p., 240 V Electric air compressor

- General lighting

- Bench lighting

- 1000 watt 120V Electric water heater

- ½ h.p. 120V Bench grinder

- 2 h.p. 240V Table saw

- 1 ½ h.p. 240V Exhaust fan

- 8000 watt 240V Thermostatically controlled electric heater

- ¾ h.p. 120V Overhead door opener

# PRACTICUM IV—IDENTIFICATION OF ELECTRICAL COMPONENTS

Fifty (50) pieces of equipment, tools, or devices from the Equipment ID list will be displayed for the contestant to identify.  Each piece will be displayed by number.

# -EXAMPLE-

# Name ____________________School________________Code/Color____ Score ________

Arkansas FFA Electrification Contest

Wiring Plan

# 200 Points

### Please read carefully

Attached is a plan for a typical utility room. It includes the following:

- Clothes dryer

- Clothes washer

- 5000W 240V hot water heater

- Freezer

5.	General purpose (lighting and convenience outlets)

.

Properly lay out a wiring plan for the utility room, using correct symbols.

Complete the circuit sheet by:

- Listing the circuit name

- Amperage of the fuse or breaker protecting the circuit

- Type, size, and number of wires for each circuit

# Score Card

#### Wiring Plan						Score

Proper Location of Devices---------------------50 points			__________

Proper Electrical Symbols----------------------50 points			__________

Circuit Name--------------------------------------20 points			__________

Circuit Breaker Amperage-----------------------30 points			__________

Wire Type------------------------------------------10 points			__________

Wire Size-------------------------------------------20 points			__________

Number of Wires----------------------------------20 points			__________

Total Points	(200)								_________

-EXAMPLE-

Revised 1/2009                                       ELECTRICAL COMPONENT

### IDENTIFICATION CARD

Contestant Name_____________________________________________________________________________

Contestant School __________________________________ Score____________________________

Directions:  Write the number opposite the tool to which it belongs.  Points will be given for each component correctly identified for a total of 200 points possible.

|  | Number |  |  | Number |  |
| --- | --- | --- | --- | --- | --- |
|  | **** | SERVICE ENTRANCE EQUIPMENT |  | **** | RECEPTACLES |
|  | 001 | Circuit Breaker Panel Box (SEP) or Subpanel |  | 040 | 120V 15A Grounded Receptacle |
|  | 002 | Entrance Ell |  | 041 | 240V Surface Mount Receptacle |
|  | 003 | Meter Base |  | 042 | 240V Flush Mount Receptacle |
|  | 004 | Service Head |  | 043 | GFCI Grounded Receptacle |
|  | 005 | Ground Rod |  | **** | BOXES |
|  | 006 | Ground Rod Clamp |  | 044 | Box Cover |
|  | **** | CONDUCTORS |  | 045 | Handy or Utility Box |
|  | 007 | #6 Gauge Grounding Wire (solid) |  | 046 | Octagon Box |
|  | 008 | #14-2 W/Ground NM Cable |  | 047 | Rectangular or Switch Box |
|  | 009 | #12-2 W/Ground NM Cable |  | 048 | Pancake Box |
|  | 010 | #12-3 W/Ground NM Cable |  | 049 | Raised Panel Cover (Mudring) |
|  | 011 | #10 Gauge THW Stranded Copper |  | 050 | Extension Ring |
|  | 012 | #6 Gauge THW Stranded Copper |  | 051 | Receptacle Cover (Weatherproof) |
|  | 013 | THW Stranded Aluminum |  | **** | SWITCHES |
|  | 014 | UF Cable ( Direct Burial) |  | 052 | Single Pole Toggle Switch |
|  | 015 | Triplex Cable |  | 053 | 3-way Toggle Switch |
|  | 016 | Bell Wire |  | 054 | 4-way Toggle Switch |
|  | **** | CONDUIT |  | 055 | Double Pole Single Throw Switch |
|  | 017 | Thinwall (EMT) Conduit Coupling(set screw) |  | 056 | Dimmer Control |
|  | 018 | Thinwall (EMT) Pressure Coupling |  | 057 | Pilot Switch |
|  | 019 | Thinwall (EMT) Pressure Connector |  | **** | TOOLS |
|  | 020 | Raintight Connector |  | 058 | Cable Ripper |
|  | 021 | Conduit Locknut |  | 059 | Test Light |
|  | 022 | Conduit Strap |  | 060 | Wire Stripper |
|  | 023 | Conduit Hub |  | 061 | Fish Tape and Reel |
|  | 024 | Thinwall (EMT) Conduit |  | 062 | Lineman’s Pliers |
|  | 025 | Liquid Tight Flexible Metal Conduit |  | 063 | Needlenose Pliers |
|  | 026 | Rigid NM Conduit (EPVC) |  | 064 | Conduit Bender |
|  | 027 | Rigid Metal Conduit |  | 065 | Pump Pliers (Channel locks) |
|  | 028 | Flexible Metal Conduit |  | 066 | Volt/Ohm/Amp Meter (Multimeter) |
|  | 029 | Flexible Nonmetallic Conduit (ENT) |  | **** | INSULATORS |
|  | 030 | 90 Degree Conduit Sweep |  | 067 | Insulator Standoff |
|  | *** | OVERCURRENT PROTECTION |  | 068 | Screw Point Insulator |
|  | 031 | Breaker, 15 Amp/120V |  | **** | MISCELLANEOUS |
|  | 032 | Breaker, 20 Amp/120V |  | 069 | Doorbell Transformer |
|  | 033 | Breaker, 20 Amp/240V |  | 070 | Grounding Clip |
|  | 034 | Breaker, 30 Amp/240V |  | 071 | Ground Wire Screw |
|  | 035 | AFCI Breaker |  | 072 | Split Bolt Connector |
|  | 036 | Time Lag Plug Fuse |  | 073 | NM Sheath Cable Box Connector |
|  | 037 | Non-Tamperable Plug Fuse |  | 074 | Wire Nut |
|  | 038 | Cartridge Fuse Blade type |  | 075 | 240V Dryer or Range Pigtail |
|  | 039 | Cartridge Fuse Ferrule Type |  | 076 | Bar Hanger |

SCORECARD

PART I	Knowledge of Subject

Written Test- 50 multiple choice questions, 2 points each-----100 points

Each team member will take test

PART II	Practicums

Practicum #1----------------------------------------------------------200 points

Wiring Diagram

Circuit Parts

Neutral--------------------------50 points

Energized-----------------------50 points

Grounding----------------------50 points

Wire Type-------------------------------10 points

Wire Size--------------------------------10 points

Number of Wires-----------------------10 points

Breaker Amperage---------------------10 points

Breaker Voltage------------------------10 points

Practicum #2-----------------------------------------------------------200 points

Wiring Practice

Insulation Removal--------------------20 points

Anchor to Box--------------------------20 points

Splices-----------------------------------30 points

Wire Loops-----------------------------20 points

Grounding------------------------------30 points

Color Code-----------------------------30 points

Amount Completed-------------------50 points

Practicum #3-----------------------------------------------------------200 points

Wiring Plan

Proper Location of Devices ----------50 points

Proper Electrical Symbols------------50 points

Circuit Name---------------------------10 points

Circuit Breaker Amperage------------30 points

Wire Type-------------------------------20 points

Wire Size--------------------------------20 points

Number of Wires-----------------------20 points

Practicum #4----------------------------------------------------------200 points

Identification of Electrical Components

50 components to be identified , 4 points each

ELECTRICITY CONTEST REFERENCE MATERIAL

The references recommended in preparing for the contest are:

- Electrical Wiring

- Understanding Electricity

- Basics of Electric Motors

- Electrical Controls

The four above references can be obtained from:

AAVIM

220 Smithonia Road

Winterville, GA 30683

1-800-228-4689

Go to www.aavim.com and you can view online.  They have additional references.

NOTE:	The latest edition of each reference will be used

# Text boxes

Source

G

~4’

4

3

3

2

1

1

1

~2’

G

NM 12-2w/g

NM 12-2w/g

NM 12-2w/g

20 amp 120V

G

ground